## Slide 1: CALIFORNIA WILDFIRE CAUSE AND EFFECT ANALYSIS
JASON LEI
JOSH GALLAGHER
THADDEUS GRAY
WAN XIA (SUSAN)
YU-HAN CHEN (AMY)

## Slide 2: Project Motivation
Motivation - With wildfires becoming an increasing problem in California, we wanted to see if we could find an trends in the causes and effects of the fires
Cause of wildfires - Weather factors - Human activities
Effects of wildfires
- Air quality - Financial cost

## Slide 3: Data Source
kaggle.com U.S. Wildfire data (plus other attributes) which has a subset of 1.88 Million US wildfire database(Year 1995 - Year 2015). We concentrate on California wildfire dataset in our analysis.
California Department of Forestry and Fire Protection Wildfire Activity Statistics (Year 2016 - Year 2019)
https://www2.purpleair.com PurpleAir, which is a real time air quality monitor, providing real time measurement of air quality on a public map.
Google Maps Platform - API

## Slide 4: Causes of Wildfires: Weather
Questions
Is there a difference between average weather on any day for a location, and the weather in the location of a fire?
Are there weather trends in the time prior to the fire being contained?

## Slide 5: Weather Data Cleaning
Limited to California
Removed fires less than 10 Acres
Removed records that did not have weather files
Removed records where temperature equaled exactly 0

## Slide 6: Weather Data Cleaning
Removed columns that would not be used
Renamed columns so Dataframe would be more aesthetically pleasing

## Slide 7: Weather Data Cleaning
Converted to Fahrenheit
Fire Duration column needed strings removed and to be turned into float for later calculations

## Slide 8: Weather Data Cleaning
Grouped data by the size of the fire
Created separate dataframes for wind, temperature, humidity, and precipitation
Took averages for time periods prior to fires’ containment

## Slide 9: Wind
Mostly grouped in 1 to 5 m/s
Duration drops significantly above 5 m/s
Lots of datapoints at 0 m/s, however none in between until almost 1 m/s. Could be error in measurements or data.

## Slide 10: Wind
* r-squared are insignificant

## Slide 11: Wind
There appears to be a consistent pattern of wind speed averages dropping until date of containment

## Slide 12: Temperature
Not much can be inferred from these graphs

## Slide 13: Temperature
* r-squared are insignificant

## Slide 14: Temperature
The temperature rises up until date of containment
Temperature averages are consistent across all fire sizes

## Slide 15: Humidity
Between 60 and 75% humidity, there is a decrease in the duration of the fires
Data clumped at 0% humidity, but none until about 10%

## Slide 16: Humidity
* r-squared are insignificant

## Slide 17: Humidity
Humidity decreases up until the date of containment
Fires 100-250 acres tend to have lower humidity

## Slide 18: Precipitation
Data for both graphs is clumped at 0 precipitation
Fires greater than 75,000 acres have little to no precipitation

## Slide 19: Precipitation
* r-squared are insignificant

## Slide 20: Precipitation
Precipitation averages are surprisingly high 30 days prior
Large fires have spike of precipitation on containment. Rainfall may have helped containment
Fires between 251 and 100 acres have much higher precipitation levels than other size groups
Could be related to storm systems with lighting causing mid-range fires
Precipitation for fires 11-250 acres is suspiciously low. Could be data error.

## Slide 21: California Wildfire Costs Analysis
What regions in California have the highest costs of wildfire damage?
What are the human causes that cause the most damage?

## Slide 22: Background
I have chosen datasets from four different years: 2019, 2018, 2017, 2016
Each data set presents the costs of human causes per Cal Fire Region
Basically, some counties are grouped in these regions, as a single Cal Fire unit can cover the entire area

## Slide 23: General Data Cleaning
Removed extraneous rows such as ”Northern Region” and ”Southern Region” as I analyzed the data with no distinction, and those rows had no data.

## Slide 24: Combining Data for First Plot
I felt it would be easier to plot all four graphs at once if I combined data into one dataframe
Specifically chose region totals for this plot

## Slide 25: Damage per Region 2019-2016
Represents total cost of wildfire damages pre region (in Billions)
There are several regions with major outliers, which is why it looks like there is missing data
Sonoma-Lake-Napa has had massive damages in three of the past four years
This area clearly is a hotspot for wildfires, with Butte, Nevada-Yuba-Placer, and Shasta-Trinity being potentially dangerous spots

## Slide 26: Damage per Region w/o Outliers
Dropped regions with the jumps in cost
Wanted to show how large the difference was between the outliers and “normal” fires

## Slide 27: Create Dataframe for Costs per Cause
Create a Dataframe to pickout the costs of damages from human causes

## Slide 28: Costs for Human Causes per Year
Represents the costs of human causes per year
Similar to costs per region, there are clear outliers
Electric power seems to be the top cause of wildfires, with three out of four years seeing significant costs
The other costly causes would be from arson and vehicle fires

## Slide 29: Costs of Human Causes per Region
Each graph represents a year
Bar plot represents major costs in human causes per region
As shown before, electric power is the primary cause for wildfires, along with arson and vehicles
Sonoma-Lake-Napa is once again the most prolific area for wildfires

## Slide 30
Effect of Wildfires: Air Quality
Is there a difference in PM2.5 (air pollutant) concentration
before and after the Woosley fire?

## Slide 31
Low-cost air sensor

## Slide 32
Data Cleaning and Processing

## Slide 33
EPA 24 hours standard: 35ug/m3
Non-wildfire season
wildfire season
Woosley Fire starts

## Slide 34: Wildfire Maps
  Questions:
  Where were the wildfires located in California?
  Where were the large scale wildfires located in California?
  (from year 1995 through year 2015)

## Slide 35: Fire Location Map - using API
Los Angeles and San Diego had slightly more fires happened during 1995 to 2015 according to the symbol map.

## Slide 36: Fire Size Heatmap - using API
The majority of large scale wildfires happened from 1995 to 2015 were close to Los Angeles and San Diego according to the fire size heatmap.

## Slide 37: Conclusions
From our analysis, the weather factors (Wind speed/Humidity/Temperature/Precipitation) have correlations with the fire size up until the date of containment, but it is unclear whether the weather impacted the fires or vice-versa
There Is a strong correlation between electrical power and wildfire costs, along with arson and vehicles. Additionally, electrical power in all areas seems to have a strong correlation with wildfires.
Wildfire increases air polution in surrounding areas

## Slide 38: Limitations and Discussions
We are not able to merge our datasets: data are from different years
Real world data cleaning: missing information or wrong information
We couldn’t find enough scientific support on some trends that we observed from data analysis
More to explore:
- Impacts from wildfires on water resources: water quality within and downstream from a burn area may be significantly impacted.
- Climate change impacts